ECE4211 HW#10R Solar Design-Pass I 03/30/2017 due 04/6/17 F. Jain Name_________

Q. 1. Design an n+-p Si solar cell for air mass m=1 (AM1).  Assume that the incident radiation for AM1 (Fig. 1) is 92.5mW/cm2.  IL=ISC = 38.97mA/cm2.

Follow cell design example of Section 6.12, page 511-518.

Given: p-Si crystalline wafer with doping of 8x1016cm-3.

n+-side: Donor concentration ND=1020 cm-3, minority hole lifetime (p=2x10-6 sec.

Minority hole diffusion coefficient Dp=12.5 cm2/sec.

p-side:   Acceptor concentration NA= 8x1016cm-3, (n=10-5sec. Dn=40 cm2/sec.

Junction area A=1 cm-2, ni (at 300K) = 1.5x1010cm-3, (r (Si)=11.8, (0=8.85x10-14 F/cm,

(=(0(r. Assume all donors and acceptors to be ionized at T=300°K.

- Find the thickness and index of refraction of the AR coating material for 0.51 micron as the average of entire spectrum.  Copy from the Design example.

Design Pass #2 Other approaches to AR coating: Surface texturing to prevent surface reflection? You may want to look at GaN LED structure (Fig. 33, p,. 316).

- List the criteria to select the thicknesses of n+ window and p-Si absorber layer. Follow Design Level-I Section 6.12.1 and Section 6.12.2.

- Determine the open circuit voltage, maximum power point Pm = Vm Im and the fill factor (FF).

- Find dominant losses:

a) Long wavelength photons h<Eg. Use value given in solved design.

b) Excess photon energy (h-Eg) not used in generating electron-hole pairs.  That is triangle J, trapezoid J ’and DF’’ Use value given in solved design for the triangle and the trapezoid. Calculate only the region DF’’

c) Voltage factor.

d) Fill factor

- Plot all the losses as a bar chart, and .show after all the above losses that the cell could be over 20% efficient.

- How would you improve the efficiency of your current cell?

Fig.1 Solar spectrum at m=0 and m=1. Same as Popquiz

Provided below are the pages 512-518 of Notes.

# 6.12 Problem set and Solutions for Solar Cell Design and Tandem Cells

6.12.1 Level 1 solar design--Q.1 Solar Cell Design: Design an n+-p Si solar cell for air mass m=1 (AM1) or AM1.5.  Assume that the incident radiation for AM1 (Fig. 1) is 92.5mW/cm2.  IL=ISC = 38.97mA/cm2.

Given: p-Si crystalline wafer with doping of 2x1017cm-3 or resistivity of ~0.1 Ohm-cm.

n+-side: Donor concentration ND=1020 cm-3, minority hole lifetime (p=2x10-6 sec. Minority hole diffusion coefficient Dp=12.5 cm2/sec.

p-side: Acceptor concentration NA= 2x1017cm-3, (n=10-5sec. Dn=40 cm2/sec. Junction area A=1 cm-2, ni (at 300K) = 1.5x1010cm-3, (r (Si)=11.8, (0=8.85x10-14 F/cm, (=(0(r. Assume all donors and acceptors to be ionized at T=300°K.

  - Find the surface reflection loss. Find the thickness and index of refraction of the AR coating material (identify the wavelength you are using in your design).  Other approaches to AR coating: Surface texturing to prevent surface reflection? You may want to do a quick literature search. (Do not spend too much time on it).

  - What are the thicknesses of the p-Si and n+ Si layers?

  - Determine the maximum power point Pm = Vm Im and the fill factor (FF).

  - Compute dominant losses:

    - Long wavelength photons h<Eg (=1.1eV).

    - Excess photon energy not used in generating electron-hole pairs.

    - FF

    - Voltage factor.

Show after all the above losses (see worked out solar design in the Notes pp. 431-443) that the cell could be 12% efficient.

  - Why an n+-n/p-p+ cell structure is better than the n+-p Si cell? Briefly show such a structure.

HINT: Follow design example pp. 431-443 for above parts. See also pp.479.

Fig.1 Solar spectrum at m=0 and m=1. (Fig. 31 from page 440 of Notes PT-II).

Q.2. For the tandem cell of Fig. 2:

(a) Compute power converted by the top cell.

  - Find the solar power that is converted by the top cell and power that is available to the bottom cell.

  - Find the open circuit voltage Voc and Vmp and Imp for each cell.

  - Find the operating current and voltage for the total tandem cell comprising of an amorphous a-Si n-p junction cell (top) and a crystalline n-p junction cell (bottom). Assume the voltage drop across tunnel junction=0.03V. Briefly sketch the tunnel junction. HINT: Pages 452 to 459. No big eqns.

Given:

- Short circuit current in the two cells is 7 mA for air mass 1.

- The top a-Si cells converts mostly photons having energy h>1.5eV and the bottom cell converts between 1.5eV> h>1.1eV and any energy not absorbed by the top cell (for h>1.5eV).

- Doping of a-Si cell is similar to that for c-Si cell. (4) (n=10-5sec Dn=0.80 cm2/sec in p type a-Si and Dp=0.25 cm2/sec and (p=2x10-6 sec in n-type a-Si layer.

| Fig. 2. Amorphous Si (top) and crystalline Si (bottom) tandem cell. | Fig. 3. The absorption coefficient in c-Si and a-Si. |
| --- | --- |

Optional Q.3. What is the advantage of a Quantum dot solar cell?

Solution Set:

Question 1 Solar Cell Design Show after all losses (excess energy loss, long wavelength photons below Eg of Si, voltage factor, and fill factor and surface reflection) the Si cell could be 12% efficient. (Design for A=1 cm2).

Contact stripe

AR coating

Junction

N+-side                                                                                                                  p-side

For AM1 condition, the incident solar spectrum generates a short circuit current of  in a cell of 1cm2 area.

- Surface reflection loss

Index of refraction of Si is

Reflectivity of Si=

Reflection Loss=Pin*0.3=27.75mW/cm2 for  or 925W/m2

Antireflection Coatings (AR) can mitigate the reflection loss.

Solar spectrum is very broad. We design a coating of thickness‘t’ with an index of refraction nr2 to eliminate reflection loss.

AR Coating

nr2

t

n-Si= 0.5m                                                                          Junction

For NA=2*1017cm-3,   =  0.1 Ohm-cm

Schematic of solar cell

(b) Determine the thickness of n+ and p-Si layers.

The thickness of n+ layer is as thin as possible. The only consideration is that series resistance Rs loss (voltage drop and power dissipation) is very small. That is Rs* Isc < 0.05V. IL=ISC = 38.97mA/cm2.

Rs < 0.05/38.97*10-3 	or, 	Rs < 1.25 Ohm.

Rs is related on resistivity  of the n+ layer (which depends on the doping concentration ND; for 1020cm-3, it is 8x10-4 Ohm-cm) ) and it’s thickness t (unknown). Here, we are neglecting the drop across p-Si thick layer d with =0.1 Ohm-cm).

Rs = L(A), A is the area of cross-section (=t*cell length 1cm) and length L is the separation between top Ohmic contact lines. Here, t (n-Si) =L/Rs

=0.1*8x10-4/(1)	=	0.8 microns. We have selected 0.5 microns which is true if the separation is less than 1mm.

The thickness of p-Si is determined by the absorption length of photons which is 2/ or 3/ where  is the absorption coefficient. Another criterion to determine the thickness d of p-Si is to keep it 2-3 diffusion length of minority electrons 2Ln-3Ln. Ln is 2x10-2 cm so 2 Ln = 4x10-2cm or 400 microns. Thickness may be small using 2/.

(c) Determine the maximum power point Vm, Im

Vm and Im are expressed as: .

Here, .

We need to find VOC to find Vm, and to find VOC we need to find the reverse saturation current Is as ISC is given to be 38.97 mA.

Is is expressed as

p-side:

n+-side: (window region)

A

=0.0259 ln[(38.97x10-3 + 0.361x10-12)/ 0.361x10-12]

VOC = 0.6579Volt

Substitute VOC and kT/q = 0.0259V in

Vm =. Since Vm is on both sides, we need to write a short program or do trial and error substitution. We know Vm is less than VOC, so we guess it to be 0.5V. for this guess we tabulate Left Hand Side (LHS) and Right Hand Side (RHS) until  the value of Vm makes both sides equal.

LHS				RHS

0.5V(first guess)		0.5799

0.57				0.5766

0.576				0.5764

0.5765V			0.5764

So Vm = 0.5765V and Im is obtained by substituting Vm in the current equation.

Im = 0.36X10-12[exp(0.5765/0.0259) -1] -38.97X10-3

=1.675x10-3 -38.97x10-3 = -37.29 mA

Two curves related to solar spectral irradiance

(d) Compute dominant losses

(i) Reflection has been computed before.

(ii) We now compute the long wavelength photons that are not absorbed. These are photons below the energy gap Eg = 1.1eV for Si. These are shown in the above Figure, in area of region 1, 2 & 3, and a triangle F’/1.1 (D) /1.16 (D’) micron point on x-axis.

The solar power in these regions is:

Region #1	68.4 W/m2

Region #2	72.69 W/m2

Region #3	35.77 W/m2

These values have been calculated in solar design before.

Region #F’DD’ power is 	16.5 W/m2 as shown below.

Total long wavelength photon loss is 193.36 W/m2 or 19.36 mW/cm2.

The % of long wavelength light loss at AM1 in Si =

(iii) We next calculate the Excess Energy Loss for photons above Eg or 1.1eV which have more energy than needed to create an electron-hole pair.

Solar spectral irradiance for AM1

Excess photon energy not utilized in electron hole pair generation

Let AM1 plot above is divided in several regions. The exact way is to find the area under the curve numerically. Regions are: Triangle , Trapezoid , Trapezoid marked as #4. These are calculated next.

Excess photon energy lost in spectral region represented by triangle

Area if the

Excess energy not used

Excess energy lost

Trapezoid #4, Rectangle #5 & Rectangle #6 can be combined by a rectangle

Excess energy =

Excess energy not used =

Total excess energy loss = 101 + 180.16 + 19 = 300.16 W/m2.

(iv) Voltage factor is defined as the ratio of VOC and Eg/q.

Voltage factor =0.6579/1.1 = 0.598.

The loss is 431.48 x 0.598 = 258.02W/m2, and the % loss is 258.02/925 = 27.89%.  This leaves available power of 173.46 W/m2.

(v) Fill Factor (FF) is defined as (VmIm)/(VOC ISC).

FF = [0.5765*37.29mA]/[0.6579*38.97mA] = 0.834 ~ 0.84.

The power loss due to FF is (1-0.84)*174.31=27.89 W/m2. The % loss is 27.89/925 = 0.03=3%.

(vi) Collection efficiency of photo-generated electrons and holes. In crystalline Si this loss may be 10%. However, it is significant in poly-crystalline Si substrates, where it is ~20%.  A 10% loss reduces the available power to (146.42 – 14.64) 131.78 W/m2.

(vii) Series resistance loss: Series resistance loss Rs and other losses (see Fig. 19b).

Bar chart of losses in Si solar cell.

# Text boxes

n+-Si

p-Si

Back contact

p-Si

d