### UConn ECE 4211, Solution SET 4 Diodes, BJTs/HBTs F. Jain, 02/17/2017

## Q.1  Briefly describe the structure and operation of following p-n junction devices: Chapter 3A

(a) Show solar cell schematic with light incidence, and V-I characteristics.

Schematic (page 204)					V-I characteristic.

(b) Showing schematically a reverse biased p-n diode and sketch its V-I characteristics.

V-I characteristics in the fourth quadrant.

(c) What is the mechanism for avalanche breakdown in the reverse biased diode shown in Fig.1?

| Fig. 1 (Fig. 8C Chapter 3A). | Fig. 9, page 121 Notes, carrier distribution under reverse biasing. |
| --- | --- |

Minority holes from n-side diffuse to the junction boundary. They get accelerated in the junction due to E field and gain energy and their impact causes creation of electron hole pairs, resulting avalanche breakdown.

(d) Fig. 2A shows a forward biased diode serving as an LED. What is the thickness of the layer where most of the injected holes recombine and photons are generated? Show LED’s V-I plot.

The layer thickness is 2Lp (two diffusion length of minority holes).

Fig. 2A. A forward biased p-n junction. 		V-I characteristics (first quadrant).

(e) Which of the two E-k diagrams you will choose for the n-region? Circle one of Fig. 2B below.

## Q.2. Fig. 3 shows a p+-n-p Si bipolar junction transistor operating in the active region.

## HINT:  A similar problem is solved on page 188.

Fig. 3.  Schematic of a p+-n-p transistor.

p+-Emitter:					n-Base:

NA = pp0= 1x1020 cm-3				ND=1 x1018 cm-3

Dn,E =30 cm2/sec.				Dp,B =7.5 cm2/sec (diffusion coefficient for holes in base)

n,E =10 sec (lifetime of injected electrons)	p,B =2 sec (holes injected from the emitter)

Emitter area AEB = 100m2 	Base-collector area: assumed to be same for simplification (it is larger in practice)

Emitter-base voltage VEB ~ 0.75 Volts (<Vbi) and it is dependent on IE.

Collector: NDC= 5x 1016 cm-3; Base-collector voltage VBC = 5 Volts (VCB= -5V reverse bias); ni= 1.5x1010 cm-3 at 300K.

(if y << 1)

(if y << 1)

Given the distribution of excess holes p(x) and holes pn(x) in the n-base as:

, 	where		(32)

(33)

Using 	(12),

## Write expression for IEP(x)

(34)

(35)

In Eq. 35, second term >> first term.

(35B)

Using ,

(35C)

## Calculate IEP at x=0 (the edge of neutral base region at the emitter-base junction) using parameters given below and assuming W=0.25x10-4cm.

Dp,B =7.5 cm2/sec (diffusion coefficient for holes in base), life time of holes p,B =2 sec, Emitter-base  area AEB = 100m2. Base doping ND=1 x1018 cm-3.		First we calculate pno,B = 225 cm-3, Lp=

## Write and expression for ICP using 		 (13)

(36)

(37)

Second term is >> than the first term.

(37B)

Using, , 		(37C)

ICP =

ICP= 4.0608*10-5 A

- Show that the base transport factor T or ICP/ IEP  is Sech(W/LP) ~ 1-W2/2(LP)2; compute its value for the transistor parameters.

Divide Eq. 37B by Eq. 35B, we get

T = ICP/ IEP  =

If ABC=AEB, 	T== Sech(W/LP).

Using series ,Sech(W/LP) ~ 1-W2/2(LP)2.

T ~ 1-W2/2(LP)2

T ~ 1-W2/2(LP)2=1-(0.25*10-4)2/[2*()] =0.999979.

Alternately, using part (b) and (c) values, T = ICP/ IEP  =8.1216*10-6 A/8.1385*10-6 A = 0.997923

- Find expression for IEN using if electron concentration n(x) in emitter is

(38) (39), ,

Or,  .

Substitution of derivative of n(x) gives us current in the p-emitter as measured from the origin at the base boundary.

IEN(x)  for x<xE , where xE is the width of emitter-base junction.

IEN(x=-xE),  						(40)

Using BJT parameters.

- Compute the ratio

From part (g) below, =

- Show using two current expressions that injection  efficiency

, using the approximation Ctnh(W/LP) ~ Lp/W when W<<LP.

Using Eq. 40 and 35C,

=

=

- What is the expression for base transit time B? Calculate its value. (Notes page 264 in BJT Design). Notes page 253 shows base transit time in an n-p-n BJT. For a p-n-p BJT we use

B= Base transit timeerev(x) = velocity of minority carriers in the base.

Value of B = (0.25*10-4)2/(2*7.5) = 4.16*10-11s for a base width of 0.25 microns.

Q. 3 Fig.4 shows the schematic of an n-p-n Si bipolar transistor with various device parameters given.

|  | Emitter n+-side: Donor concentration ND=1020 cm-3, minority hole lifetime (pE=2(10-6 sec. Minority hole diffusion coefficient Dp,E=12.5 cm2/sec. Base p-side: Acceptor concentration NA,B=5x1017 cm-3, (nB=10-5 sec. Dn,B=40 cm2/sec Effective mass: electrons me=mn=0.26mo, holes mh=mp= 0.64 mo,Junction area base-emitter ABE=10-3 cm-2, base-collector 8x10-3 cm-2 Collector n-side: ND,Collector = 1015 cm-3, minority hole lifetime (pC=2(10-6 sec. Minority hole diffusion coefficient Dp,C=15 cm2/sec. ni (300K)=1.5(1010 cm-3. (r(Si)=11.8, (0=8.85(10-14 F/cm, (s=(r(0. |
| --- | --- |
| Fig. 4 An n-p-n transistor. |  |

3(b) Find collector current ICN using the electron distribution np(x) at x=W at the base boundary at the base-collector junction.

3(c) From above two components find the base transport factor T ICN/IEN.

Q3(d) Obtain the common base current gain  (=T*for the BJT after computing emitter-base injection efficiency using computed value of transport factor T.