UCONN ECE 5212  		09/20/16, Due in two weeks, F. Jain

HW4 Finite barrier quantum well energy levels

Q. 1. (a) Determine the electron and hole (both light and heavy) energy levels and wavefunctions in the well of an AlxGa1-xAs-GaAs multiple quantum well layer.  Assume well thickness of 50Angstrom.   Use 30% aluminum in AlGaAs.   Assume energy band discontinuity Ec/Ev ratio to be 60 to 40 in conduction and valence bands, respectively.

(b) What is the effective well width Leff of an infinite well which would give the same location of the first level in the conduction band as in the finite well problem done above in part (a). Given:

Effective masses: GaAs well 			AlGaAs barrier [mhh=heavy holes, mlh=light holes]

me =0.0665mo		me =0.0916mo		Electrons

mhh = 0.34 mo		mhh = 0.466 mo	Heavy holes

mlh = 0.094 mo		mlh = 0.107 mo		Light holes

Eg as a function of aluminum fraction AlxGa1-xAs =1.424 +1.247 (x)

Reference: Notes pp. 70-78.

Q1. Hint/Solution attached

Write your program and confirm the values shown in the solution/hint set.